## Slide 1
Submitted by Tahsinul Haque Dhrubo & Ankhi Akter Mim | CSE424: Pattern Recognition
Bathroom activities monitoring for older adults by a wrist-mounted
accelerometer using a hybrid deep learning model
BRAC University

## Slide 2
Overview
Major sections of this paper presentation
Introduction
Methodology and Materials
Results
Discussion
Abstract
Problem
Analysis
Conclusion

## Slide 3
Abstract
  Evaluate health conditions for older adults
  Wrist-mounted accelerometer
Monitoring activities of daily life
Dressing, undressing, brushing teeth, using the toilet, washing face, and washing hands
Six bathroom activities
A hybrid convolutional neural network (CNN) model
Cross-validation (LOSO),
MLP, SVM, KNN, DT
f1-score for using toilet was improved from 0.7784 to 0.8437

## Slide 4
Clinical relevance
This provides a model that helps monitoring older adults’ bathroom activities using a single wrist-mounted accelerometer

## Slide 5
PROBLEMS
SOLUTIONS
Introduction

## Slide 6
1 | 2 | 3
Age-related diseases such as cardiovascular diseases and cancers | Not concerned about activities of daily life (ADL) | Couldn't remember the activities of daily life
Problems

## Slide 7
1 | 2 | 3
Monitor and Control the diseases | Use of Deep Learning as CNN | Hybrid CNN model to recognize bathroom activities using hand crafted features and raw data from the accelerometer.
Solutions

## Slide 8
Data acquisition
An Empatica E4 wristband was used for collecting
data.
  Integrated with a 3-axis accelerometer, with a sampling frequency of 32 Hz and a detectable range of ±2g.
  The dominant hand and annotate six bathroom activities
  Six bathroom activities accounted for 49.4 hours in total
METHODOLOGY AND MATERIALS

## Slide 9
Signal pre-processing
Signal pre-processing included two stages: filtering and magnitude extraction
  Filtering: Two Butterworth low-pass filters were applied to the original acceleration signals
  Magnitude extraction : M = root(ax2 + ay2 + az2)
METHODOLOGY AND MATERIALS

## Slide 10
Hand-crafted features extraction
Features were extracted from each component, using a sliding window of 32s (1024 samples) with 50% overlap.
  detailed coefficients of the third to sixth levels of the wavelet transform were included
  407 features were extracted
METHODOLOGY AND MATERIALS

## Slide 11
Classification models
Four traditional machine learning models and two deep learning models were applied
  Support Vector Machine (SVM)
  Multilayer perception (MLP) (hidden layers=3, [1:1:10])
  K-nearest neighbor (KNN) (K=3, [3:2:35])
  Decision tree (DT) (maximum depth=33, [1:1:35])
METHODOLOGY AND MATERIALS

## Slide 12
Training and testing methods
The models were trained in two scenarios
  LOSO
  LOSO and transfer learning
METHODOLOGY AND MATERIALS

## Slide 13
Results
Classification performance of LOSO
the f1-scores of six models based on
LOSO,

## Slide 14
Results
Classification performance of LOSO
The hybrid CNN obtains the highest f1-scores for all bathroom activities

## Slide 15
Results
Classification performance of LOSO
The main confusion occurs between others and each of six bathroom activities.

## Slide 16
Results
Classification performance of LOSO
f1- scores for the 15 subjects using the hybrid CNN model.

## Slide 17
Results
Classification performance of transfer learning
The confusion matrix of transfer
learning using the hybrid CNN model

## Slide 18
Models comparison
The MLP, SVM, KNN, and DT have hand-crafted features as input while the hybrid CNN model fuse the hand-crafted features and CNN-based features
Discussion
Activity recognition
This part will only discuss the activity classification results of the hybrid CNN model.

## Slide 19
Transfer learning
According to the comparison between the results of LOSO and transfer learning, the subject-dependent models show higher f1-scores
Discussion

## Slide 20
Conclusion
This study is aimed to recognize the bathroom activities of
older adults using a wearable accelerometer by deep learning
methods.

## Slide 21
Thank you!
Tahsinul Haque Dhrubo & Ankhi Akter Mim